## Slide 1: Gesture Controlled Robot
Team 16
09005060 D V Deepankar Reddy
09005070 M A Haseeb Ajmal
09005073 Gaurav Singh Chauhan
09005075 Ravi Vishwakarma

## Slide 2: Problem Statement
Control the firebird and gripper using gestures
i.e.
Detect user gestures using kinect
Convey these gestures as signals to firebird
Make firebird/gripper take appropriate actions

## Slide 3: Requirements
Interpret a subset of gestures as commands.
(Control Left and right motors separately)
Transmit these commands to the robot.
Write code for signal handling on firebird.
Write the code for robot in RTOS.
Control the movement of the robot based on these signals.

## Slide 4: Project Plan
Stage 1: Installing the appropriate software kits and getting the kinect to do basic joint detection.
Stage 2: Implementing static gestures.
Stage 3: Implementing continuous gestures.
Stage 4: Optimizing the code/logistics for better performance(faster response, finer/more accurate motion)
Work Division : Groups of 2 switching between tasks (effectively handling each module) to gain complete understanding and feel of the project.

## Slide 5: State Chart
jkl
KINECT/LAPTOP
FIREBIRD
Waiting for mode
Waiting for gesture
in mode
Transition
gesture
Transition
Gesture
Mode specific
gesture & n frames
since last signal sent
Send signal
Signal Sent
Waiting mode
signal
Action
Action Complete
Waiting for signal
in mode
Mode signal
Mode signal
Signal received

## Slide 6: Tasks Completed -- Gestures
Implemented bot control using gestures in 3 modes, each mode separated by a transition gesture.
Mode 1:
  For Long range motion of the bot.
  Implemented static gestures for:
    Forward motion
    Backward motion
    Stop
  -- Also Implemented continuous angle detection , i.e.
  When you rotate your right arm by an angle, appropriate calculations are done (both magnitude and direction) and sent to the bot.

## Slide 7: Gestures - 2
Mode 2:
  For fine control of the bot.
  Similar to steering a JCB Proclainer.
  Right hand controls the right motor and left the left
  The distance moved by the hand is proportional to the shaftcount of the corresponding motor

## Slide 8: Gestures - 3
Mode 3:
  For controlling the gripper.
  The position of your arms is mapped directly to that of the gripper arms.

## Slide 9: Communication and Control
Commands/data were transmitted to the robot wirelessly using Zigbee devices.
The commands/data received were interpreted and actions were carried out accordingly.
Scaled down the data values sent to fit the range of zigbee (0-128).

## Slide 10: RTOS issue
We wanted to do the c-code in RTOS
If the gestures are only forward,backward,left, right then RTOS works fine
But if you want to do shaft encoding (for angular rotation) it does not work
Reason : We were not able find the function to handle nested interrupts
And also in case of nested interrupts RTOS just drops the nested interrupt that occurs leading to desynchronization

## Slide 11: Challenges - Kinect
Data from kinect:
Problem:
  Data received from kinect fluctuated a lot from frame to frame.
  So sending continuous data caused lot of problems.
  (For eg: If the angle to be rotated kept fluctuating the bot would have to rotate continuously giving jerks and damage the motors.)
Solution:
  Data was sampled for every 10 frames and sent only if
  the variation was significant.(Set a threshold value)

## Slide 12: Challenges - Zigbee
Data sent over zigbee:
Problem:
  Data sent over zigbee should be between 0-128.
  This was clearly insufficient to transmit angles (+ve & -ve)
Solution:
  Reducing the frame rate so that the data to be sent never exceeds the limits (0-128)
  (You can only move so much within a small time)
  2. Scaling down the data to fit the range.

## Slide 13: Challenges - Synchronization
Sending sets of values
Problem:
  A set of values to be acted upon had to be sent one after another due to limitation of zigbee.
  The processing speeds of laptop and firebird are different.
  So when the action corresponding to a set of values is being performed (by bot), if the next set arrives (one by one), depending upon the time at which the firebird is again ready to handle the signals, the signals received get interpreted differently.
  Thus the behaviour of firebird becomes unpredictable.
Solution:
  Introduce delays between sending each value.
  An optimal delay had to be decided by lot of experimentation so that the reaction of the bot to a gesture wasn’t slow.

## Slide 14: Test Cases
Test 1
Criteria : Sampling (Deciding the no. of frames after which data has to be sent to the bot)
Description : Experimented with different values of no. of frames
Performance Metrics:
  Data Fluctuations/Accuracy
  Continuity of data

## Slide 15: Test Cases
Test 2:
Criteria: Synchronization(Deciding the delay to be introduced between sending continuous data)
Description : Experimentation with different values
Performance Metrics:
  Delay in observing the response on the bot
  Proper interpretation of signals

## Slide 16: Re-usability features
Modularity of Gestures,Signal processing:
  Divided the entire class of gestures into different modes each one dealing with a different aspect of control.
  Controlling an entirely different thing can be done by specifying a gesture for transition into the new mode and writing code specific to the mode.
  Same applies to code on firebird.
The code for gestures is modular and hardware independent and could be extended to building a library.

## Slide 17: Future Enhancements
NUI can be used to control lots of other bots besides firebird thus getting greater functionality.
The speech feature of kinect can be put to use.
Use of bluetooth instead of zigbee to solve the synchronization problem without delays.
Building a gesture library for kinect.